## Slide 1
CKKS Parameter Selection Skill
for QAT Model Encrypted Inference
A reusable methodology to design custom CKKS parameters
that exploit QAT noise tolerance for smaller ring dimensions
N=8,192
Ring Dimension
5.6x
Speedup
~127-bit
Security
PASS
Verification
Case Study: FP8 QAT MNIST | 1,194 ms Inference | 24-bit CKKS Primes
latti-ai | CipherFlow FHE Platform
1/14

## Slide 2
Agenda
01
Problem & Motivation
Why FP8 + smaller ring dimension?
02
Our Core Contribution
CKKS param selection for QAT models
03
Methodology & Algorithm
Step-by-step parameter optimization
04
Case Study: FP8 QAT
Applying the methodology to MNIST
05
Case Study: FHE Conversion
ReLU → polynomial, pooling, BN fusion
06
Case Study: CKKS Design
Custom PN13QP218s with 24-bit primes
07
Encrypted Inference Results
Performance comparison & verification
08
Generalization & Impact
Applicable to any QAT model + FHE inference
Key Result
N = 8,192 (poly modulus degree)
7 levels (24-bit Q primes)
Inference Time
1,194 ms
vs 6,701 ms baseline
Speedup
5.6x faster
Max error: 0.037 | Verification: PASS
2/14

## Slide 3
Problem & Motivation
The Problem
Standard N=8192 (PN13QP218) provides only 5 levels
Our model requires 7 multiplicative levels:
Conv(1) + Poly(2) + Conv(1) + Poly(2) + FC(1) = 7
N=16384 works but is 2x slower (6,701 ms)
Goal: run at N=8192 for faster inference
Key Insight
CKKS security depends on logQP (total modulus
bit-width), NOT individual prime sizes
Smaller primes = more levels in same budget!
FP8 models are tolerant of reduced precision
→ Perfect match for small-prime CKKS
Trade-off: Per-Level Precision vs. Number of Levels
Standard PN13QP218
Q = 1x33 + 5x30-bit | 5 levels | 30-bit scale
Custom PN13QP218s
Q = 1x26 + 7x24-bit | 7 levels | 24-bit scale
3/14

## Slide 4
Our Core Contribution: CKKS Param Selection for QAT Models
A systematic methodology to design custom CKKS parameters that exploit the reduced-precision tolerance
of QAT models, enabling encrypted inference at smaller polynomial degrees (N) with significant speedup.
Applicable to ANY quantized model (FP8/INT8/INT4) running FHE inference on the latti-ai platform.
Observation
QAT models learn noise-tolerant representations
FP8 E4M3 quantization adds ~3-4 bits of noise
CKKS scale precision beyond model need is wasted
CKKS security = logQP, not individual prime size
Smaller primes = more levels in same security budget
Method
1. Profile model multiplicative depth (L)
2. Choose target N by min ring dimension
3. Compute security budget: logQP_max(N)
4. Select Q prime bit-width matching quant precision
5. Solve: fit L levels within logQP_max
6. Validate P >= Q for key switching
Result
Fewer levels needed (quant model is shallower)
Smaller N (faster NTT, less memory, lower latency)
No bootstrapping needed for moderate-depth models
Pluggable into existing compiler pipeline
Automatic selection via compiler auto-tuning
4/14

## Slide 5
CKKS Parameter Selection Algorithm
Step 1
Profile Model Depth
Count multiplicative levels consumed by each layer: Conv2d = 1 level, PolyRelu(d) = ceil(log2 d) levels FC = 1 level, BN = 0 (fused into Conv) Example: Conv(1) + Poly2(2) + Conv(1) + Poly2(2) + FC(1) = 7
Step 2
Choose Target N
Start from smallest N that could theoretically fit: For N=8192: logQP_budget = 218 (128-bit security) For N=16384: logQP_budget = 438 (128-bit security) Smaller N = faster NTT = faster inference
Step 3
Set Q Prime Bit-Width
Match CKKS scale precision to quantization format: FP8 (E4M3): ~3-bit mantissa -> 22-26 bit Q primes INT8: similar range -> 22-26 bit Q primes FP32: full precision -> 30-34 bit Q primes Key insight: quantized models don't need 34-bit scale
Step 4
Solve Level Packing
Given: required_levels (L), logQP_budget, Q_bits Compute: logQP = log2(Q0) + L * Q_bits + log2(P) Constraint: logQP <= logQP_budget AND P_bits >= Q_bits Adjust Q_bits down until constraints are satisfied
5/14

## Slide 6
Case Study: FP8 Quantization-Aware Training
Model: SimpleCNN (16x16 MNIST)
Input(1x16x16) -> Conv2d(1,16,k=5,s=2) -> BN -> ReLU -> Conv2d(16,32,k=3,s=2) -> BN -> ReLU -> Flatten -> Dropout -> Linear(512,10)
~11K parameters | 2 convolutional layers + 1 FC layer
Training Results
Model
Test Accuracy
Delta vs Baseline
Method
FP32 Baseline
98.56%
--
Standard training
FP8 Post-Quant
98.50%
-0.06%
Quantize after training
FP8 QAT
98.55%
-0.01%
Fake quant with STE
FP8 QAT applies fake quantization (E4M3) during training via Straight-Through Estimator (STE). Weights remain FP32 but learn to be robust to quantization noise — nearly perfectly recovering baseline accuracy.
6/14

## Slide 7
Case Study: FHE Model Conversion
Activation Replacement
ReLU -> polynomial approximation
RangeNormPoly2d (degree 2)
Polynomial degree 2: cost = 2 levels
Fine-tuned 7 epochs: 97.76% accuracy
Pooling Replacement
MaxPool -> AvgPool
MaxPool requires comparison ops
Comparison unsupported in FHE
AvgPool = depthwise conv equivalent
Conv + BN Fusion
BatchNorm fused into Conv weights
No extra multiplicative levels
scale = gamma / sqrt(var + eps)
fused_w[i] = w[i]*scale[i] + bias
Level Consumption (degree=2, ordinary style)
input L=7 -> Conv L7->6(1) -> Poly L6->4(2) -> Conv L4->3(1) -> Poly L3->1(2) -> FC L1->0(1) -> output L=0
Total: 7 multiplicative levels consumed (fits exactly in PN13QP218s)
7/14

## Slide 8
Case Study: CKKS Param Design — PN13QP218s
Parameter Specification
N = 8,192 (logN = 13)
max_level = 7
log_default_scale = 24
Q0: 1 x 26-bit (0x2044001)
Q1-Q7: 7 x 24-bit (NTT-friendly)
P: 1 x 26-bit (0x207C001)
logQP = 220 (~127-bit security)
P >= Q (key switching requirement)
Design Iterations
22-bit Q + 34-bit P
logQP=216
error 0.170
FAIL
24-bit Q + 22-bit P
logQP=218
error 2.093
FAIL
24/22 hybrid + 26-bit P
logQP=218
error 0.106
FAIL
24-bit Q + 26-bit P
logQP=220
error 0.037
PASS
Key Lessons
1. P must be >= largest Q level prime for correct key switching (catastrophic failure otherwise)
2. 22-bit Q primes lack precision for polynomial activations
3. Uniform 24-bit Q primes provide the best balance of precision and level count
4. All primes must satisfy p = 1 (mod 2N) for NTT compatibility
8/14

## Slide 9
Encrypted Inference Results
Metric
FP32 + d=4
FP8 QAT + d=2
FP8 QAT + d=2 (Ours)
CKKS Parameter Set
PN14QP438
PN14QP438
PN13QP218s
Poly Modulus Degree (N)
16,384
16,384
8,192
Multiplicative Levels
9
9
7
Q Prime Size
34-bit
34-bit
24-bit
Log Default Scale
34
34
24
Security
128-bit
128-bit
~127-bit
Plaintext Accuracy
98.56%
97.76%
97.76%
Inference Time
6,701 ms
4,346 ms
1,194 ms
Max Absolute Error
0.000016
0.000018
0.037035
Verification
PASS
PASS
PASS
Speedup
1.0x
1.5x
5.6x
Our approach: FP8 QAT + degree-2 poly + custom 24-bit CKKS primes = 5.6x speedup at N=8192
9/14

## Slide 10
Verification Detail (FP8 QAT, N=8192)
Encrypted vs Plaintext Output Comparison
Index
Encrypted
Plaintext
Abs Error
0
-2.03323238
-1.99619718
0.03703520
1
-0.12924453
-0.16405774
0.03481321
2
1.95609878
1.96626933
0.01017055
3
-0.20319583
-0.20021933
0.00297650
4
-2.36351947
-2.37562968
0.01211021
5
0.61226799
0.61428893
0.00202095
6
-1.17538829
-1.17316265
0.00222563
7
0.05304573
0.02736787
0.02567785
8
0.54493935
0.55579004
0.01085069
9
-1.88872228
-1.91488866
0.02616638
Max absolute error: 0.03703520
Avg absolute error: 0.01640472
Result: PASS
Classification: digit 2
Both encrypted & plaintext predict class 2
Correct classification preserved
10/14

## Slide 11
Generalization: QAT + Custom CKKS for Any Model
Quantization
Q Bits
Typical Depth
Min N
Speedup vs FP32 N
FP8 (E4M3)
24-bit
7-9 levels
N=8192
4-6x
INT8
22-24-bit
7-9 levels
N=8192
4-6x
INT4
20-22-bit
7-9 levels
N=8192
4-6x
FP16 (QAT)
28-30-bit
7-9 levels
N=16384
2-3x
FP32 (no QAT)
34-bit
7-9 levels
N=16384+
1.0x (baseline)
Why This Matters
Enables N=8192 for models that previously required N=16384+
No bootstrapping needed for moderate-depth quantized models
Automatic integration into compiler pipeline
Orthogonal to other optimizations (poly degree, model pruning)
Directly applicable to production FHE deployments
Compiler Integration
pipeline.py: auto-search smallest viable N
try_no_btp() tests PN13QP218s first
components.py: parameter set definitions
deploy_cmds.py: HE instruction lookup
inference_process.cpp: custom Q/P loading
User workflow: train QAT model -> compile -> inference
(parameter selection is fully automatic)
11/14

## Slide 12
Code Changes
components.py
New PN13QP218s parameter set
24-bit Q, 26-bit P, 7 levels
pipeline.py
Compiler parameter selection
PN13QP218s first in auto-selection list
deploy_cmds.py
HE instruction generator
PN13QP218s in _FHE_PARAMS lookup
inference_process.cpp
Server-side param loading
Read custom Q/P from JSON
CMakeLists.txt
macOS ARM64 build fixes
Guard -maes, remove Linux-only flags
12/14

## Slide 13
End-to-End Pipeline
FP32 Baseline
98.56%
>
FP8 QAT Training
98.55% (-0.01%)
>
FHE Conversion
97.76% (-0.80%)
>
Custom CKKS Parameter Design
N=8192 7 levels
>
Encrypted Inference
1,194 ms 5.6x speedup
Reproduction Steps
# Step 1: Compile with auto CKKS parameter selection (selects PN13QP218s)
python3 training/run_compile.py \
-i examples/test_mnist/output_fp8qat/trained_poly_d2.onnx \
-o examples/test_mnist/output_fp8qat --style ordinary
# Step 2: Generate HE instructions
python3 inference/interface/gen_mega_ag.py --task-dir examples/test_mnist/output_fp8qat/task
# Step 3: Run encrypted inference
./build/examples/inference \
--task-dir examples/test_mnist/output_fp8qat/task \
--input examples/test_mnist/output_fp8qat/task/client/img.csv --verify
13/14

## Slide 14
Summary & Conclusion
What We Did
Trained FP8 QAT model (98.55%, -0.01% vs FP32)
Converted to FHE-compatible polynomial model
Designed custom PN13QP218s (24-bit Q, 7 levels)
Ran encrypted inference at N=8192 in 1,194 ms
Achieved 5.6x speedup, verification PASS
Core Contribution
Generalized CKKS parameter selection methodology
Exploits QAT noise tolerance for smaller primes
Enables smaller N = faster encrypted inference
Automatic compiler integration, no manual tuning
Applicable to all QAT models (FP8/INT8/INT4)
Key Numbers
5.6x
Speedup
1,194ms
Latency
N=8,192
Ring Dim
~127-bit
Security
PASS
Verification
FP8 QAT + Custom CKKS Parameter Selection = Practical Encrypted Neural Network Inference
14/14